## Slide 1: Network Layer
Chris O’Brien

## Slide 2: Overview
Overall, Layer 3 is responsible for routing packets from one node to another between networks.
Primary jobs of the Network Layer include:
  Logical addressing
  Routing
  Encapsulation
  Fragmentation and reassembly
  Error handling

## Slide 3: Logical Addressing
Each node that wants to send or receive information outside their network must have a logical address. Structure for organizing nodes on a network.
  Uses the IPv4 or IPv6 protocol
Addresses are assigned statically or dynamically via a DHCP server.
  Statically assigned machines generally include devices like servers and printers whereas dynamically assigned machines are for host machines.
L3 uses logical IP addresses (can change at will).
L2 uses MAC addresses, burned into NIC (theoretically cannot change).

## Slide 4: Logical Addressing (cont.)
Current most used protocol is IPv4.
  Addresses are 32 bits in size, broken up into 4 octets or groups of 8 bits
  Uses dotted decimal notation for humans to read and has a binary equivalent which is how the computer reads the address
  There are up to 2^32 or 4.19 billion addresses available

## Slide 5: Logical Addressing (cont.)
Will eventually go to IPv6
  128 bits in size
  Consists of eight groups of four hexadecimal digits separated by colons
  There are up to 2^128 or 3.4 x10^38 addresses available
    That is ~ 4.8×10^28 addresses per PERSON as of today whereas IPv4 provides less than one address per person.

## Slide 6: Routing / Encapsulation
Router takes the information from Layer 4 (Transport) and adds (or appends) the Layer 3 header. It then sends the packet to Layer 2 (Data Link).
  This process is called data encapsulation and provides the necessary information for the Network layer
  The Layer 3 header includes many fields but the most important are the source and destination IP addresses

## Slide 7: Routing / Encapsulation (cont.)
In addition to encapsulating, the network layer must be able to direct, or route, the information. Sometimes the source and destination hosts are not on the same network. The device routing the information finds the best path to take based on different things. The paths between networks are called “hops” and the router determines which hops will provide the most efficient way to travel between networks based on:
  Quality of Service (QoS)
  Cost
  Network congestion

## Slide 8: Fragmentation and Reassembly
Network layer’s main responsibility is to deliver data between networks. After encapsulation, data is passed to the Data Link layer. The problem is, sometimes the message being sent is too large for the maximum frame size at Layer 2. If this happens, the network layer will divide the message into multiple fragments that are sent individually and reassembled on arrival of the destination network layer. For an Ethernet frame, the maximum payload size is generally 1500 bytes.
  As shown in the image, we have a message that is 4,464 bytes. The Layer 3 device splits, or fragments, it into four separate units which will be sent at 1500 bytes or less each. When it reaches the destination Layer 3 device, it will then be reassembled to the full 4,464 bytes.

## Slide 9: Error Handling
Internet Control Message Protocol, or ICMP, is used between operating systems of network computers to send error messages. It is a unique protocol because it operates at the network layer and isn’t used to exchange data. It is merely used to provide feedback and is not always reliable.
  ICMP is used by the popular diagnostic tools ping and traceroute